## Slide 1
Final Detailed Configuration |  | 
Parameter | Non-Stop Aircraft | One-Stop Aircraft
Interior |  | 
Passenger Mix (1st class/Business/Economy) | 12 / 42 / 171 | 18 / X / 207
Seat Pitch (in) (1st class/Business/Economy) | 60 / 38 / 32 | 40 / X / 32
Seat Depth (in) (1st class/Business/Economy) | 28 / 25 / 25 | 28 / X / 25
Seat Recline (in) (1st class/Business/Economy) | 43 / 36 / 32 | 36 / X / 32
Bulkhead to Seat Nose (in) (1st class/Business/Economy) | 24 / 20 / 18 | 22 / X / 20
Aisle Width (in) (1st class/Business/Economy) | 25 / 20 / 18 | 10 / X / 15
Number of Galley Carts (1st class/Business/Economy) | 4 / 9 / 13 | 5 / X / 16
Galley Size (in) | 15 x 36 | 15 x 36
Number of Lavs (1st class/Business/Economy) | 1 / 1 / 3 | 1 / X / 4
Lav Size (in) | 38 x 40 | 38 x 40
Entry Door Size (in) | A: 42w x 72h | A: 42w x 72h
Emergency Door Size (in) | I: 24w x 48h | I: 24w x 48h
Final Detailed Configuration |  | 
Parameter | Non-Stop Aircraft | One-Stop Aircraft
Engine/Nacelle |  | 
Inlet Diameter (ft) | 9.6 | 7.6
Length (ft) | 23 | 18.2
Fuel Tank |  | 
Tank Volume (ft^3) | 1677 | 1276
Span Wise/Spar Location (ft) | 0.2 / 0.8 | 0.2 / 0.7
Landing Gear |  | 
Nose Gear Tire Size | 44 x 14 | 40 x 14
Main Gear Tire Size | 56 x 16 | 44 x 16
Aft CG Angle (deg) | 21.9 | 22.5
Tip Back Angle (deg) | 19.4 | 19.4
Cargo |  | 
Cargo Container | LD-W | LD-W
Number of Containers | 6 | 3
Total Cargo Volume (ft^3) | 502 | 251
Final Detailed Configuration |  | 
Parameter | Non-Stop Aircraft | One-Stop Aircraft
Main Wing |  | 
Sweep (deg) | 37 | 31
Taper Ratio | 0.35 | 0.35
Aspect Ratio | 7.9 | 9.5
Planform Area (ft^2) | 2567 | 2224
Span (ft) | 142 | 145
Root Chord (ft) | 26.8 | 22.7
MAC (ft) | 14.5 | 12.3
Wing Dihedral (deg) | 6 | 6
Horizontal Tail |  | 
Sweep (deg) | 42 | 36
Taper Ratio | 0.35 | 0.35
Aspect Ratio | 4 | 4
Planform Area (ft^2) | 395 | 351
Span (ft) | 39.8 | 37.5
Root Chord (ft) | 14.7 | 13.9
MAC (ft) | 8 | 7.5
Wing Dihedral (deg) | 9.6 | 9
Vertical Tail |  | 
Sweep (deg) | 42 | 36
Taper Ratio | 0.5 | 0.5
Aspect Ratio | 1.6 | 1.6
Planform Area (ft^2) | 281 | 301
Span (ft) | 21.2 | 22
Root Chord (ft) | 17.7 | 18.3
MAC (ft) | 5.9 | 6.1